Volumes and Concentrations

Concentrations

1 dm3 = 1000 cm3 = 1000ml = 1L

moles = concentration (mol dm^-3) times volume ( dm^3 ) or n = cv

Making A standard Solution
1. moles = concentration * volume
2. Calculate the Mr of the substance
3. calculate the actual mass needed (mass = Mr * moles)
4. Add that mass of the substance into the volume of the solvent

Volumes At RTP

RTP is:
- 25 °C
- 100-101 kPa
At RTP, 1 mole of gas occupies exactly 20dm3
So the formula is:

moles = { volume (dm^3) } over { 24 dm^3 "or" 24000 cm^3 } n = v over { 24 "or" 24000 }

Volumes Not At RTP

For volumes outside of RTP, we use the ideal gas equation, which is:
pressure ( pa ) times volume ( m^3 ) = moles times 8.314 Jmol^-1K^-1 times temperature ( K ) or pV = nRT

This assumes that the gas particles:
- Are moving randomly
- Have elastic collisions (no energy loss as heat, noise, etc)
- Have negligible size
- Have no intermolecular forces

Conversions
- Pa = kPa * 1000
- K = C + 273
- M3 = cm3 * 10-6
- DM3 = cm3 * 10-3